## Slide 1
NETWORK COMMUNICATION PRESENTATION / TEAM 06
TCP/IP Communication in Action
Following the data when a user opens a secure website, from the browser to the web server and back
Speakers and responsibilities
01
Mariam Blessing Ajao
Team Lead, 1st speaker
Introduction + Application layer
02
Wisdom Binichiuku Odili
2nd speaker
Transport layer + TCP/UDP: how the connection is established
03
Beverlyn Ewuradwoa Amanfu
3rd speaker
Internet layer, addressing and network devices
04
Richard Inyang
4th speaker
Encapsulation, decapsulation and the OSI mapping
05
Fokemg-yalie Brisco Elias
5th speaker
Troubleshooting process
01
Notes: Mariam Blessing Ajao (Team Lead, 1st speaker) opens the presentation. Scenario: opening a secure website. Decorative artwork reused from the Module 2 model deck.

## Slide 2
TEAM 06 / TCP/IP IN ACTION
The TCP/IP model and its four layers
02
A layered framework that explains how data moves between devices. Each layer has one job.
TCP/IP has four layers; the OSI model has seven.
Notes: Introduction: TCP handles reliable delivery between applications; IP handles addressing and routing. Source: RFC 9293, RFC 791, Cisco Networking Academy.

## Slide 3
TEAM 06 / TCP/IP IN ACTION
Scenario: opening a secure website
03
A user types https://www.icdfa.edu.ng in the browser and presses Enter.
01
Enter URL
User types the address in the browser
02
Read URL
Browser interprets the address
03
DNS lookup
Domain name becomes an IP address
04
TCP connect
Three-way handshake to port 443
05
HTTPS request
TLS-protected HTTP request is sent
06
Response
Server replies along the reverse path
Data is encapsulated as it moves down the layers on the client, and decapsulated as it moves up the layers at the web server.
Notes: Mariam: the scenario and the basic journey User, Browser, Network, Web Server, Response.

## Slide 4
TEAM 06 / TCP/IP IN ACTION
Application layer: how the communication starts
04
DNS: finding the IP address
1
Client checks its local DNS cache
2
If needed, a query goes to a DNS resolver
3
Resolver returns the IP address
4
Browser uses it to contact the web server
Like phone contacts: select a name and the phone finds the number. DNS does this for website names.
HTTPS: HTTP protected by TLS
HTTP carries web content between browser and server. TLS protects the channel.
Confidentiality
Helps stop others simply reading the traffic
Integrity
Helps detect unauthorised changes to data
Authentication
Helps the browser verify the server’s identity
DNS, HTTP and HTTPS belong to the TCP/IP Application layer.
Notes: Mariam. Sources: RFC 1034, RFC 1035, RFC 9110, RFC 8446.

## Slide 5
TEAM 06 / TCP/IP IN ACTION
Application layer: protocols and the OSI model
05
Protocol | Meaning | Purpose
DNS | Domain Name System | Finds the IP address of a domain
HTTP | Hypertext Transfer Protocol | Transfers web content
HTTPS | Hypertext Transfer Protocol Secure | Protects web communication using TLS
TCP/IP
Application
OSI
Application
Network services to applications
OSI
Presentation
Data representation, encryption, compression
OSI
Session
Establishes, manages and ends sessions
TLS functions sit near OSI Presentation/Session, though modern stacks do not map one-to-one.
Notes: Mariam. The TCP/IP Application layer corresponds mainly to the OSI Application, Presentation and Session layers.

## Slide 6
TEAM 06 / TCP/IP IN ACTION
Transport layer: the TCP three-way handshake
06
Client / browser
Web server
SYN
Client asks to connect
SYN-ACK
Server acknowledges, sends its own SYN
ACK
Client acknowledges: connection established
After the handshake, HTTPS/TLS communication can begin.
Destination port: TCP 443
Identifies the HTTPS service on the server
Source port: ephemeral
A temporary port chosen by the client’s operating system
Reliability
Sequence numbers, acknowledgements and retransmission keep data complete and in order
Notes: Wisdom. Source: RFC 9293. Port numbers plus IP addresses identify the communication endpoint.

## Slide 7
TEAM 06 / TCP/IP IN ACTION
TCP compared with UDP
07
Feature | TCP | UDP
Connection | Connection-oriented; uses a handshake | Connectionless; no TCP-style handshake
Reliability | Acknowledgements, retransmission and ordered delivery | No TCP-style guaranteed delivery or ordering
Speed / overhead | More overhead from connection and reliability mechanisms | Lower overhead; suits small or time-sensitive traffic
Example uses | Traditional HTTPS over TCP, file transfer, email protocols | DNS queries, streaming, real-time apps, HTTP/3 via QUIC
UDP is not simply a faster TCP. It is a different service model.
Notes: Wisdom. HTTPS normally uses TCP port 443; HTTP/3 uses QUIC over UDP (RFC 9000).

## Slide 8
TEAM 06 / TCP/IP IN ACTION
Internet layer: addressing, routing and devices
08
IP addressing
IPv4
Four decimal numbers, e.g. 192.168.1.50
IPv6
Hexadecimal with colons, e.g. 2002:db8::1
Private / public
Private inside local networks; public is routable online
Source → destination
Sender’s IP to the web server’s IP, found through DNS
Network devices
Router
Reads the destination IP and forwards packets between networks
Switch
Connects devices inside a local network
Wi-Fi access point
Gives wireless access to the local network
ISP
Carries traffic from the local network to the wider Internet
Notes: Beverlyn. Source: RFC 791. 192.168.1.50 is an example private address.

## Slide 9
TEAM 06 / TCP/IP IN ACTION
Packet journey: client to web server
09
REQUEST
User device
Browser
Wi-Fi AP / switch
Local network
Router
Forwards by IP
ISP
Provider network
Internet routers
IP routing
Web server
HTTPS : 443
RESPONSE
Web server
HTTPS : 443
Internet routers
IP routing
ISP
Provider network
Router
Forwards by IP
Wi-Fi AP / switch
Local network
User device
Browser
The router reads the destination IP and forwards the packet. The response follows the same path back and is decapsulated at the user’s device.
The packet may pass through several routers before reaching the web server.
Notes: Beverlyn. Request: user computer, router, ISP, Internet, web server. Response: the reverse path.

## Slide 10
TEAM 06 / TCP/IP IN ACTION
IP address vs MAC address
10
Feature | IP address | MAC address
Other name | Logical address | Physical address
Layer | Internet layer | Network Access layer
Purpose | Identifies the network location of a host | Identifies a network interface on the local link
Example | 192.168.1.50 | A1:B4:C5:DD:C1:3E
Used for | Routing between networks | Local network / frame delivery
IP address = where the device is on the network. MAC address = which interface is addressed on the local link.
Notes: Beverlyn. IP addressing matters for the end-to-end journey; MAC addressing is used for local-link delivery.

## Slide 11
TEAM 06 / TCP/IP IN ACTION
Complete view: encapsulation and decapsulation
11
Sending device
Web server
Application
HTTPS data
Application
HTTPS data
Transport
TCP segment
Transport
TCP segment
Internet
IP packet
Internet
IP packet
Network Access
Frame
Network Access
Frame
Network
Encapsulation
Headers added
Decapsulation
Headers removed
Each layer adds the information needed to deliver the data.
Each layer removes and processes its information, until the web server gets the HTTPS request.
Sending device | Down the layers
Receiving device | Up the layers
Notes: Richard. Sending device: data moves down the layers, each adding information. Receiving device: each layer removes and processes its information on the way up.

## Slide 12
TEAM 06 / TCP/IP IN ACTION
Troubleshooting: the website does not load
12
1
Check IP configuration
ipconfig or ip addr
2
Test the default gateway
ping gateway IP
3
Test external connectivity
ping 8.8.8.8
4
Check DNS resolution
nslookup or dig
5
Check destination and routing
Route and router reachability
6
Check TCP port 443
Blocked, refused or dropped?
7
Check firewall rules
Client, network, router, server
8
Capture packets
Wireshark, if still unclear
9
Interpret the TCP handshake
SYN, SYN-ACK, ACK or RST
10
Test the website again
Confirm the fix
Reading the handshake
Repeated SYNs, no SYN-ACK
Possible connectivity, firewall, routing or server issue. Needs further investigation.
Immediate RST
The destination may be refusing the connection.
SYN, SYN-ACK, ACK
Handshake completes, HTTPS/TLS starts and the page loads.
Notes: Fokemg-yalie. Repeated SYNs alone do not identify the exact cause; further investigation is required.

## Slide 13
TEAM 06 / TCP/IP IN ACTION
Reference
13
Thank you.
Internet Engineering Task Force (IETF). (2022). RFC 9110: HTTP Semantics.
Cisco Networking Academy. Introduction to Networking / TCP/IP Networking Model. Cisco Press
Rescorla, E. (2018). RFC 8446: The Transport Layer Security (TLS) Protocol Version 1.3. IETF.
Mockapetris, P. (1987). RFC 1034: Domain Names – Concepts and Facilities.
Internet Engineering Task Force (IETF), RFC 9293 – Transmission Control Protocol (TCP).
NIST, Computer Security Resource Center – networking and cybersecurity reference materials.
Notes: Sources: RFC 9110 (HTTP), RFC 8446 (TLS 1.3), RFC 1034/1035 (DNS), RFC 9293 (TCP), RFC 791 (IP), RFC 9000 (QUIC); Cisco Networking Academy, Introduction to Networking; NIST CSRC.